## Slide 1
Industrial Safety
Industrial hazards and the organisation of safe work.
Lifting equipment, pressure equipment and electrical installations.
Accident prevention, worker actions and production control.
A training course for work in the Republic of Kazakhstan.
Industrial Safety
01
Notes: Обучение Промбезу Общий.ppt
промышленная безопасность.docx

## Slide 2
What the course covers
General requirements apply across production operations.
Each equipment section covers documentation, authorisation and protective measures.
Practical scenarios help identify conditions that require work to stop.
Equipment-specific authorisation is arranged separately.
Industrial Safety
02
Notes: Обучение Промбезу Общий.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx
Презентация вебинара Сосуды под давлением.pptx
Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 3
Purpose of industrial safety
Industrial safety protects people, property and the environment from hazardous production factors.
Accident prevention begins before equipment starts.
Emergency preparedness includes communication, evacuation and rehearsed personnel actions.
Safety must be maintained throughout the equipment life cycle.
Industrial Safety
03
Notes: Обучение Промбезу Общий.ppt
https://old.adilet.zan.kz/rus/docs/Z1400000188

## Slide 4
Regulatory framework
The Kazakhstan Law on Civil Protection establishes general requirements.
Order No. 359 covers lifting equipment; Order No. 358 covers pressure equipment.
Electrical safety and hot work are governed by their specific rules.
Work instructions account for the equipment and site conditions.
A sample instruction cannot replace requirements for the actual task.
Industrial Safety
04
Notes: Обучение Промбезу Общий.ppt
промышленная безопасность.docx
https://adilet.zan.kz/rus/docs/V1400010332
https://old.adilet.zan.kz/rus/docs/V1400010303
https://old.adilet.zan.kz/rus/docs/V1500010889
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 5
Hazardous production facilities
Hazardous substances and processes require checking the criteria for a hazardous facility.
Identification follows legislation rather than the everyday name of a business.
Hazardous technical devices are assessed according to their type and parameters.
Workers must know their area's hazards and the limits of their authorisation.
A facility name without the word hazardous does not remove the risk.
Industrial Safety
05
Notes: Обучение Промбезу Общий.ppt
https://old.adilet.zan.kz/rus/docs/Z1400000188

## Slide 6
Hazardous substances and processes
Combustible substances can ignite; oxidisers intensify combustion.
Toxic substances are hazardous through inhalation and contact.
Pressure, temperature and mechanical energy can cause severe injury.
Work requires information about the substance, process and protective measures.
Hazards depend on properties and handling conditions.
Industrial Safety
06
Notes: Обучение Промбезу Общий.ppt
промышленная безопасность.docx

## Slide 7
Accidents and incidents
Destruction, an uncontrolled explosion or a hazardous release can indicate an accident.
Equipment failure or a process deviation can constitute an incident.
An event must be reported and examined even if nobody is injured.
Concealing a deviation prevents the organisation from averting a later accident.
Record deviations before they recur.
Industrial Safety
07
Notes: Обучение Промбезу Общий.ppt
https://old.adilet.zan.kz/rus/docs/Z1400000188

## Slide 8
Duties of the organisation
The organisation maintains equipment and meets mandatory requirements.
It appoints responsible persons and establishes control procedures.
It arranges training, knowledge assessment and personnel authorisation.
It maintains readiness to contain accidents and deal with their consequences.
Appointing a responsible person does not remove the organisation's duties.
Industrial Safety
08
Notes: Обучение Промбезу Общий.ppt
https://old.adilet.zan.kz/rus/docs/Z1400000188

## Slide 9
Worker actions
Workers perform assigned tasks within their training and authorisation.
They check the workplace and use the specified protective equipment.
They report defects, deviations and threats to people.
In immediate danger, they stop work and move to safety.
Do not attempt an unauthorised repair of a dangerous fault.
Industrial Safety
09
Notes: Обучение Промбезу Общий.ppt
промышленная безопасность.docx

## Slide 10
Training and authorisation
Training explains hazards and safe work methods.
Knowledge assessment verifies understanding of requirements.
A briefing addresses the actual task and workplace.
Practical preparation and authorisation are required where stipulated by the rules and task.
Viewing a presentation does not authorise every operation.
Industrial Safety
10
Notes: Обучение Промбезу Общий.ppt
Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 11
Production control
Control identifies breaches before an accident occurs.
Checks cover equipment, documentation, personnel and working conditions.
Each finding receives an action, an owner and a deadline.
Closure requires verification that the issue has actually been corrected.
A closed finding needs confirmation on site.
Industrial Safety
11
Notes: Обучение Промбезу Общий.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 12
Checks before starting work
Clarify the task, work-zone boundaries and responsible persons.
Check equipment, protective devices and clear access routes.
Assess neighbouring activities and possible changes in conditions.
Do not begin until unsuitable conditions have been corrected.
Yesterday's good condition does not replace today's check.
Industrial Safety
12
Notes: промышленная безопасность.docx
Презентация вебинара Грузоподъемные механизмы Ким.pptx
Презентация вебинара Сосуды под давлением.pptx

## Slide 13
Workplace risk assessment
Identify what could cause harm and who could enter the danger zone.
Prefer hazard elimination and engineering protection.
Organisational measures and PPE provide additional protection.
Repeat the assessment when equipment, tasks or surroundings change.
Changed conditions require a new assessment.
Industrial Safety
13
Notes: промышленная безопасность.docx
Обучение Промбезу Общий.ppt

## Slide 14
Work permits and coordination
Use a work permit where required by the rules and established procedures.
Specify the location, task, personnel and protective measures.
Actual workplace conditions must match the conditions of authorisation.
A changed task requires review of the permit conditions, not an informal agreement.
A signature on a permit does not replace completed protective measures.
Industrial Safety
14
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx
промышленная безопасность.docx

## Slide 15
Isolation of energy sources
Before maintenance, identify electrical, mechanical and stored energy.
Stop equipment and prevent unintended starting.
Release pressure and secure moving parts under the established procedure.
Authorised personnel verify the absence of hazardous energy.
The Stop button alone does not isolate energy.
Industrial Safety
15
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx
Презентация вебинара Сосуды под давлением.pptx

## Slide 16
Hot work
Welding, cutting and heating produce sparks and hot surfaces.
Remove combustible materials or protect them using the specified method.
Check adjacent rooms, openings and concealed spaces.
Provide firefighting equipment and post-work monitoring.
Sparks can travel beyond the visible work area.
Industrial Safety
16
Notes: промышленная безопасность.docx
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 17
Equipment documentation
The equipment passport identifies the device and its permitted parameters.
The manufacturer's manual defines operating and maintenance conditions.
Logs preserve inspection, repair and defect records.
Establish unknown parameters before operating equipment.
A nearby device's parameters cannot replace the equipment passport.
Industrial Safety
17
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx
Презентация вебинара Сосуды под давлением.pptx

## Slide 18
Lifting equipment
Cranes, hoists and other lifting devices have different applications.
Slings, lifting beams and containers form part of the lifting system.
Equipment selection depends on load mass, the work zone and installation conditions.
Plan the operation using the equipment passport and lifting procedure.
Safe lifting depends on the entire system.
Industrial Safety
18
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 19
Lifting equipment passport and markings
Check the equipment type and identification number.
Verify lifting capacity, installation conditions and manufacturer restrictions.
Check inspection records and authorisation for use.
Clarify illegible or contradictory markings.
Verify lifting capacity for the actual operating conditions.
Industrial Safety
19
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx
https://adilet.zan.kz/rus/docs/V1400010332

## Slide 20
Recording and maintaining lifting equipment
State registration or internal recording requirements depend on the device type.
Exemption from state registration does not remove control obligations.
Maintain and repair equipment according to the established schedule.
Document inspections and the correction of defects.
Internal records also require clear responsibility.
Industrial Safety
20
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 21
Responsibilities during crane operations
Supervision oversees safe operation.
The person responsible for serviceable condition organises maintenance and repair.
The person responsible for load handling organises the safe lifting operation.
The crane operator and slinger fulfil their duties and use agreed signals.
Responsibilities must be understood before lifting begins.
Industrial Safety
21
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 22
Preparing a lift
Determine the load mass, centre of gravity and attachment points.
Select equipment and accessories with suitable characteristics.
Check the route, landing area and absence of people.
Agree on communication between participants.
Establish an unknown load mass before lifting.
Industrial Safety
22
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 23
Slings and lifting accessories
Check identification and suitability for the chosen lifting arrangement.
Inspect ropes, chains, sling legs, hooks and connections.
Remove damaged or unidentifiable accessories from service.
Protect load edges using the specified padding.
A knot in a sling is not a repair.
Industrial Safety
23
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 24
Lifting danger zone
Keep people out of the area where a load could fall or move.
Do not allow anyone beneath a suspended load.
Do not guide a load by hand while positioned between it and an obstacle.
Maintain the zone boundaries throughout the operation.
A short lift presents the same hazard.
Industrial Safety
24
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 25
Signals and stopping
Agree on clear signals and the communication method in advance.
Stop movement if communication is lost.
A stop signal concerning danger to people requires an immediate response.
Resume only after the cause is resolved and actions are coordinated.
Do not guess the meaning of an unclear signal.
Industrial Safety
25
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 26
Inspection of lifting equipment
Shift inspections, maintenance and technical examinations serve different purposes.
Check the structure, mechanisms, brakes and protective devices.
Determine intervals and scope from the applicable rules and equipment documentation.
Do not bypass a defective limiter to finish a shift.
Protective devices are part of the conditions for safe operation.
Industrial Safety
26
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 27
Testing and repairing lifting equipment
Qualified specialists conduct tests under the established programme.
A test load does not authorise overloads during normal operation.
Certain repairs or modifications require additional examination.
Record the results and authorisation for continued operation.
A trial lift cannot replace the required post-repair examination.
Industrial Safety
27
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 28
Welded joints in lifting equipment
Repair safety-critical components using an established procedure.
Determine welder, material and inspection requirements for the structure.
Cracks, deformation and unacceptable defects require specialist assessment.
Unauthorised welding can alter structural behaviour.
Repair of a load-bearing structure requires a specific decision.
Industrial Safety
28
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 29
Scenario: a damaged sling
A sling is defective, but the load must be moved urgently.
Do not begin the lift; notify the responsible person.
Prevent further issue of the accessory pending the required decision.
Continue with suitable, serviceable equipment.
Urgency does not change acceptance criteria.
Industrial Safety
29
Notes: Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 30
Pressure equipment
Boilers, vessels, pipelines and cylinders contain stored energy.
Loss of containment can cause a release, burns or harmful exposure.
Risk depends on pressure, temperature and the working medium.
Operate each device within its established limits.
A small vessel is not necessarily a low-hazard vessel.
Industrial Safety
30
Notes: Презентация вебинара Сосуды под давлением.pptx
https://old.adilet.zan.kz/rus/docs/V1400010303

## Slide 31
Operating and design parameters
Operating, design, permitted and test pressures serve different purposes.
Test pressure applies to an established test procedure.
Use the documented and authorised operating limits.
Observe temperature restrictions and medium compatibility.
A test parameter is not an operating parameter.
Industrial Safety
31
Notes: Презентация вебинара Сосуды под давлением.pptx
https://old.adilet.zan.kz/rus/docs/V1400010303

## Slide 32
Vessel classification and applicable rules
Classification depends on parameters and the nature of the medium.
Pressure alone is insufficient for a universal assessment.
A specialist determines applicable requirements and inspection scope.
Operators use the established restrictions for their own equipment.
Classification affects inspection and documentation.
Industrial Safety
32
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 33
Protective devices
Safety devices limit dangerous parameter exceedances.
Their condition and settings require established checks.
Do not bypass, blank off or alter protection without authorisation.
Investigate the cause of a protective trip.
Protection is not intended to compensate continually for an incorrect operating mode.
Industrial Safety
33
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 34
Monitoring pressure and temperature
Compare instrument readings with the permitted operating conditions.
Check for visible damage and unreliable readings.
Replace a faulty instrument under the established procedure.
Respond to leakage, vibration or unusual noise as instructed.
One normal reading is insufficient when other danger signs are present.
Industrial Safety
34
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 35
Starting and monitoring operation
Confirm equipment readiness and authorisation before starting.
Check valves, protection and the required instruments.
Change parameters in the sequence specified by the instructions.
Respond to deviations as instructed; do not guess settings.
Starting after repair requires confirmed readiness.
Industrial Safety
35
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 36
Stopping and preparing for maintenance
Isolate equipment from pressure sources and hazardous media.
Release pressure and verify a safe condition.
Clean, purge and test the atmosphere where required.
Begin work after completing protective measures and authorisation.
A faulty gauge reading zero does not prove safety.
Industrial Safety
36
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 37
Technical examination of vessels
Inspection and testing assess technical condition.
Intervals depend on the device and applicable requirements.
Do not start work when an examination is overdue; notify the responsible person to arrange the examination and authorisation.
Record the results in the equipment documentation.
Do not copy an inspection interval from a different vessel.
Industrial Safety
37
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 38
Compressed gas cylinders
Identify the gas using markings and documentation.
Protect cylinders against falling, heat and valve damage.
Use compatible regulators and serviceable connections.
Never check leaks with an open flame.
Do not connect a cylinder with uncertain identification.
Industrial Safety
38
Notes: Презентация вебинара Сосуды под давлением.pptx
Сварщик.ppt

## Slide 39
Repairing and welding vessels
Repair only after safe removal from service.
The procedure, personnel and inspection must suit the vessel's purpose.
Do not weld a container with unidentified residual contents.
Return to service requires documented inspection results.
An apparently empty container may retain explosive residues.
Industrial Safety
39
Notes: Презентация вебинара Сосуды под давлением.pptx
Сварщик.ppt

## Slide 40
Scenario: rising pressure
Pressure rises and normal control fails to restore the operating conditions.
The operator follows the emergency shutdown instructions.
Move people out of danger and notify the responsible person.
Do not bypass protection or repair equipment under pressure.
Investigate the cause after making the situation safe.
Industrial Safety
40
Notes: Презентация вебинара Сосуды под давлением.pptx

## Slide 41
Electrical hazards
Current, electrical arcs and hot components can cause severe harm.
Moisture, damaged insulation and conductive surfaces increase danger.
The absence of sparks or noise does not establish absence of voltage.
Restrict access to electrical installations under the established procedure.
Voltage can remain dangerous without any advance sensation.
Industrial Safety
41
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 42
Personnel categories and authority
Duties and electrical safety qualification groups determine permitted actions.
A group does not authorise every task without an assignment and authorisation.
Only authorised personnel connect, repair and switch equipment.
Learners must remain within the limits of their preparation.
Knowing a term does not authorise an operation.
Industrial Safety
42
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx
https://old.adilet.zan.kz/rus/docs/V1500010889

## Slide 43
Organising work in electrical installations
Determine the required form of authorisation for the specific task.
Appoint responsible persons and the work team.
The person admitting the team checks workplace preparation and gives a briefing.
Record breaks, relocation and completion under the established procedure.
The actual work must match the assigned task.
Industrial Safety
43
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx
https://old.adilet.zan.kz/rus/docs/V1500010889

## Slide 44
Work with voltage removed
Authorised personnel carry out the necessary disconnections.
They prevent unintended energisation and display prohibition notices.
They verify absence of voltage and install the required earthing.
They install the necessary barriers and other notices.
Disconnecting and verifying absence of voltage are different actions.
Industrial Safety
44
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 45
Earthing and protective conductors
The protective conductor is part of the shock-protection system.
Repair damaged connections before work.
Do not replace a protective conductor with an improvised metal connection.
Specialists carry out checks and repairs.
An intact-looking enclosure does not prove effective protection.
Industrial Safety
45
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 46
Portable equipment
Inspect the enclosure, cable, plug and connections before use.
Select equipment for the environment and follow its instructions.
Stop using equipment with a damaged cable or signs of overheating.
An improvised connection does not replace a serviceable assembly.
Check condition before switching on.
Industrial Safety
46
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 47
Electrical protective equipment
Select protection for the voltage and nature of the work.
Before use, check integrity and required test markings.
Do not use damaged equipment or equipment with overdue tests.
PPE does not permit bypassing organisational measures.
An unknown test date requires verification.
Industrial Safety
47
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 48
Work near live parts
Determine boundaries and safe distances for the actual installation.
Maintain them for tools, loads and equipment parts as well as people.
Do not move barriers without authorisation.
If conditions change, stop work until protective measures are reviewed.
Dangerous approach does not require direct contact.
Industrial Safety
48
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 49
Returning electrical equipment to service
Verify completion and removal of people from the danger zone.
Remove temporary protective measures in the established sequence.
Record completion and authorisation to energise.
Authorised personnel carry out energisation.
A trial start requires the same safety controls.
Industrial Safety
49
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 50
Scenario: a damaged cable
A portable tool has an exposed conductor.
Stop using it and prevent further energisation.
Notify the responsible person to arrange repair or replacement.
Do not touch the damage or repair the cable while energised.
Applying tape alone does not authorise continued use.
Industrial Safety
50
Notes: Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 51
Emergency notification
Report the location, hazard and known information about casualties.
Use the site's established communication channels; call 112 or 101 where needed.
Do not delay reporting while independently searching for the cause.
Warn nearby people without exposing yourself to danger.
The report must enable responders to locate the danger quickly.
Industrial Safety
51
Notes: промышленная безопасность.docx
Обучение Промбезу Общий.ppt

## Slide 52
Evacuation and assembly point
Use a safe escape route appropriate to the hazard.
Do not return for belongings or enter a closed-off zone.
At the assembly point, report your presence and known missing persons.
Return only when authorised after conditions have been assessed.
Report immediately if a person's whereabouts are unknown.
Industrial Safety
52
Notes: промышленная безопасность.docx
Обучение Промбезу Общий.ppt

## Slide 53
Safety when giving assistance
First make sure the rescuer is not exposed to danger.
Call emergency services and describe the situation.
Act within your training and follow the dispatcher's instructions.
Do not enter a hazardous atmosphere or touch an energised casualty without appropriate protection.
A second casualty makes rescue more difficult.
Industrial Safety
53
Notes: промышленная безопасность.docx
Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 54
Reviewing an event and restarting
Preserve information about signs, timing and circumstances.
Establish causes from facts, including organisational conditions.
Verify corrective measures before resuming work.
Inform personnel about changes to instructions and equipment.
Restart requires correction of the cause, not just the consequences.
Industrial Safety
54
Notes: Обучение Промбезу Общий.ppt

## Slide 55
Final knowledge assessment
Work requires a clear task, serviceable equipment and valid authorisation.
Lifting defects, pressure leaks and electrical damage require timely stopping.
Emergency actions begin with protecting people and raising the alarm.
Select Start test.
If conditions are uncertain, wait for verification before working.
Industrial Safety
55
Notes: Обучение Промбезу Общий.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx
Презентация вебинара Сосуды под давлением.pptx
Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx