## Slide 1
Welder
Fundamentals of welding processes and safe workplace organisation.
Joint preparation, equipment, protection and inspection.
A training programme for work in the Republic of Kazakhstan.
This course does not automatically award a vocational grade.
Welder
01
Notes: Сварщик.ppt

## Slide 2
Course content
The course covers arc welding, gas flame processes and equipment.
Separate sections address electrical, gas and fire hazards.
Practical scenarios connect preparation, execution and completion.
The welding procedure specifies parameters for the actual task.
Welder
02
Notes: Сварщик.ppt

## Slide 3
Purpose of a welded joint
Welding creates a permanent joint between materials.
Required properties depend on the material, structure and operating conditions.
Weld appearance does not verify all internal properties.
Acceptance follows the requirements for the specific product.
Structural safety depends on joint quality.
Welder
03
Notes: Сварщик.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 4
Main processes
An electric arc provides heat in arc welding.
Gas welding uses the flame of fuel gas and oxygen.
Weld-pool protection depends on the selected process.
Select the process according to material, thickness and procedure.
One set of parameters cannot apply to every process.
Welder
04
Notes: Сварщик.ppt

## Slide 5
Manual metal arc welding
The consumable electrode contributes to the weld metal.
Its coating provides the intended process protection.
Select the electrode classification, diameter and parameters using the welding procedure.
Electrode condition affects joint quality.
Damp or unsuitable materials must be replaced.
Welder
05
Notes: Сварщик.ppt

## Slide 6
Gas-shielded welding
The process uses wire or a non-consumable electrode, depending on its type.
Gas shields the weld pool from the surrounding atmosphere.
Interrupted gas supply can impair quality.
Select the gas and flow rate according to the procedure and equipment.
Shielding gas can displace oxygen from the work area.
Welder
06
Notes: Сварщик.ppt

## Slide 7
Gas welding and cutting
The torch or cutting torch must match the gas used.
Gas welding and oxygen cutting perform different tasks.
Select parameters and equipment according to the material and manufacturer's instructions.
Use the lighting and shutdown sequence for the actual equipment.
There is no universal pressure setting for all torches.
Welder
07
Notes: Сварщик.ppt

## Slide 8
Task documentation
Read the drawing and joint requirements before work.
Establish the material, edge preparation and welding position.
Check the procedure, parameters and inspection requirements.
Clarify unclear requirements before welding starts.
An informal assumption cannot replace the specified procedure.
Welder
08
Notes: Сварщик.ppt

## Slide 9
Preparing components
Clean surfaces as required by the procedure.
Remove contamination that could impair quality or produce harmful emissions.
Check edge shape and joint gap.
Secure components for stable positioning and safe access.
Assess an unknown coating before heating it.
Welder
09
Notes: Сварщик.ppt

## Slide 10
Assembly and tack welds
Verify component alignment against the drawing.
Make tack welds according to material and procedure requirements.
Fixtures must hold components without dangerous movement.
Remove unacceptable tack-weld defects using the established method.
Tack welds also affect joint quality.
Welder
10
Notes: Сварщик.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 11
Parameters and sequence
Select current, voltage and travel speed using the procedure.
Account for welding position, thickness and the component's thermal condition.
Any parameter change must be justified.
Pass sequence helps control shape and distortion.
Guessing parameters is especially dangerous for safety-critical structures.
Welder
11
Notes: Сварщик.ppt

## Slide 12
Welding power sources
Transformers, rectifiers and inverters have different characteristics.
Verify power supply and permitted load against the equipment passport.
Follow the cooling and duty-cycle instructions.
Stop in the event of overheating or a fault.
A compact machine still requires correct connection.
Welder
12
Notes: Сварщик.ppt

## Slide 13
Cables and electrode holder
Check insulation, connections and electrode clamping.
Protect cables from heat, cuts and moving vehicles.
Place the holder to prevent accidental short circuits.
Remove defective components from use.
Correct damaged insulation before energising.
Welder
13
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 14
Work return conductor
Current must return through the intended welding circuit.
Provide a reliable connection to the workpiece.
Do not substitute random pipes or structures for the return conductor.
Apply the special insulation requirements in fire or explosion hazardous conditions.
The welding circuit and protective earthing serve different purposes.
Welder
14
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 15
Permanent and temporary welding stations
A permanent station is equipped for repeated operations.
A temporary station requires assessment of the actual task location.
Access, lighting and equipment positioning must be safe.
Coordinate nearby activities before starting.
Moving the machine creates a new workplace.
Welder
15
Notes: Сварщик.ppt

## Slide 16
Main welding hazards
The arc creates radiation and electrical shock hazards.
Sparks and hot metal cause burns and fires.
Fumes and gases affect breathing.
Handling components, noise and awkward posture create additional risks.
Select protection for all hazards of the task.
Welder
16
Notes: Сварщик.ppt

## Slide 17
Eye and face protection
Select a welding helmet or shield for the process and parameters.
The filter must provide the required protection.
Check integrity, attachments and function.
Use protection against flying particles during grinding and cleaning.
Ordinary glasses cannot replace a welding filter.
Welder
17
Notes: Сварщик.ppt

## Slide 18
Clothing and hand protection
Clothing must protect against sparks and hot particles.
Use welding gloves and keep them dry.
Prevent exposed skin and pockets that collect sparks.
Footwear and clothing arrangement must keep hot metal out.
Clothing contaminated with combustible substances is unsuitable.
Welder
18
Notes: Сварщик.ppt

## Slide 19
Protecting other people
Separate the welding area with the specified screens.
Prevent unprotected people from looking directly at the arc.
Check where sparks and particles travel.
Keep access routes clear and easy to identify.
Arc hazards extend beyond the welding station.
Welder
19
Notes: Сварщик.ppt

## Slide 20
Fumes and ventilation
Remove contaminants as close to their source as possible.
General ventilation supplements local extraction.
Emissions depend on the metal, coatings and consumables.
Select respiratory protection from a risk assessment; it does not replace required ventilation.
The absence of a strong smell does not prove clean air.
Welder
20
Notes: Сварщик.ppt

## Slide 21
Electrical safety for welders
Authorised personnel connect the machine using the established method.
Check protective connections and cables before work.
Do not work with damaged equipment or unsafe moisture conditions.
Repairs and switching require the relevant separate authorisation.
An electrical safety group does not authorise every operation.
Welder
21
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V1500010889

## Slide 22
Pre-shift checks
Clarify the task, documentation and authorisation.
Inspect the machine, cables, fixtures and protective equipment.
Check ventilation, screens and fire precautions.
Correct deficiencies before welding.
The check applies to today's location and task.
Welder
22
Notes: Сварщик.ppt

## Slide 23
Preparing hot work
Obtain the prescribed authorisation for temporary hot work.
Remove or protect combustible materials.
Check openings and adjoining spaces.
Provide firefighting equipment and the required monitoring.
Sparks can cause smouldering out of sight.
Welder
23
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 24
Oxygen and fuel gases
Oxygen supports combustion and increases fire hazards.
Fuel gas can form a dangerous mixture with air.
Keep oxygen fittings free from oil and grease.
Never use oxygen to blow off clothing or ventilate a space.
Each gas requires compatible equipment.
Welder
24
Notes: Сварщик.ppt

## Slide 25
Identifying a cylinder
Identify the gas from markings and documentation.
Check the shell, valve and required examination information.
Do not use a defective or uncertainly identified cylinder.
Colour alone is not sufficient for connection.
Uncertainty about the contents rules out connection.
Welder
25
Notes: Сварщик.ppt
Презентация вебинара Сосуды под давлением.pptx

## Slide 26
Positioning and moving cylinders
Secure cylinders against falling and protect them from heat.
Use equipment intended for cylinder handling.
Do not lift by the valve or expose cylinders to impacts.
Determine separation distances and co-location from current requirements.
Valve damage can cause a sudden release.
Welder
26
Notes: Сварщик.ppt
Презентация вебинара Сосуды под давлением.pptx

## Slide 27
Regulators and gauges
Select a regulator for the gas and pressure range.
Use compatible connections without improvised adapters.
Check gauge condition and absence of damage.
Set operating pressure according to the torch instructions.
A value from someone else's example is not a setting.
Welder
27
Notes: Сварщик.ppt

## Slide 28
Hoses and connections
Use hoses suitable for the gas and working conditions.
Protect them from kinks, sparks and mechanical damage.
Use the specified fasteners for connections.
Check leaks by an approved method without an open flame.
A smell or suspected leak requires stopping.
Welder
28
Notes: Сварщик.ppt

## Slide 29
Flashback and protection
Flashback carries the flame back towards the gas system.
Specified valves and flashback arrestors reduce the risk.
Stop according to the instructions after a pop, overheating or unstable operation.
Restart only after establishing and correcting the cause.
A safety device does not replace a serviceable system.
Welder
29
Notes: Сварщик.ppt

## Slide 30
Welding containers
Before heating, establish what the container previously held.
Remove residues and isolate connected services under the procedure.
Test the atmosphere and complete the required authorisation measures.
Do not independently weld a closed or unidentified container.
An apparently empty container may contain flammable vapours.
Welder
30
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 31
Confined spaces
Entry requires special preparation and established authorisation.
Arrange atmosphere testing, ventilation, communication and an attendant.
Plan rescue without improvisation.
Stop and leave if conditions change.
Shielding gas can create an oxygen-deficient atmosphere.
Welder
31
Notes: Сварщик.ppt

## Slide 32
Work at height
Use a safe platform and the specified fall protection.
Select attachment points under the established system, not arbitrarily.
Protect fall-protection components from sparks and hot metal.
Barrier off the lower area against falling objects and particles.
A random scaffold component is not a verified anchorage.
Welder
32
Notes: Сварщик.ppt

## Slide 33
Handling components
Determine mass and the handling method beforehand.
Use suitable lifting equipment and stable supports.
Keep hands clear of potential trapping points.
Identify hot components and place them safely.
Metal appearance does not always reveal its temperature.
Welder
33
Notes: Сварщик.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 34
Making the weld
Maintain the parameters and sequence specified by the procedure.
Monitor process stability and equipment condition.
Carry out the required cleaning between passes.
Do not continue if equipment fails or protection is lost.
Stop for unsafe conditions before a defective joint results.
Welder
34
Notes: Сварщик.ppt

## Slide 35
Visible joint defects
Cracks, undercut, overlap and unfilled craters require assessment.
Weld size and shape must match the documentation.
Porosity and lack of penetration can have different causes.
Determine acceptance from requirements, not personal impressions.
Grinding does not prove removal of an internal defect.
Welder
35
Notes: Сварщик.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx

## Slide 36
Inspection and repair
Supplement visual inspection with the required methods.
Record results against the specific joint.
Use an agreed procedure for repair.
Repeat inspection to confirm the repair result.
Unauthorised repair can conceal the cause of a defect.
Welder
36
Notes: Сварщик.ppt
Презентация вебинара Грузоподъемные механизмы Ким.pptx
Презентация вебинара Сосуды под давлением.pptx

## Slide 37
Breaks and completion
Shut down equipment and the gas system as instructed.
Prevent unintended starting and leaks.
Inspect the work area and adjacent spaces for smouldering.
Record completion and maintain the required fire monitoring.
Cooling and concealed smouldering require attention after welding.
Welder
37
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 38
Faults or leakage
Stop work and carry out a safe shutdown.
Warn people and notify the responsible person.
Do not search for gas leaks with a flame or repair under pressure.
Resume only after the cause has been confirmed as corrected.
Repeated popping is not normal operation.
Welder
38
Notes: Сварщик.ppt

## Slide 39
Fire and emergency notification
Report the exact location and nature of the hazard.
Call for help under the established procedure; use 112 or 101 where necessary.
Maintain a safe escape route.
Attempt firefighting only with suitable training and safe conditions.
Evacuate when fire threatens to spread.
Welder
39
Notes: Сварщик.ppt
https://old.adilet.zan.kz/rus/docs/V2200026867

## Slide 40
First aid and safety
First stop harmful exposure without endangering yourself.
Call emergency services and act within your training.
For electrical injury, do not touch the person until electrical exposure is safely removed.
Do not enter a hazardous atmosphere without protection to attempt rescue.
Assistance requires safe conditions.
Welder
40
Notes: Сварщик.ppt
Презентация вебинара Электробезопасность - Ким - ноябрь 2025 года.pptx

## Slide 41
Scenario: an unidentified container
You are asked to weld an attachment onto a used container.
Its previous contents are unknown.
Stop until identification, preparation and authorisation are complete.
External cleanliness does not prove absence of hazardous residues.
Heat only after safe conditions are verified.
Welder
41
Notes: Сварщик.ppt

## Slide 42
Final knowledge assessment
The welding procedure determines materials, preparation and parameters.
Check equipment and protective measures before work.
Faults, leaks and changed conditions require stopping.
Select Start test.
Safe completion is part of every welding task.
Welder
42
Notes: Сварщик.ppt